BULLETIN                                             April ‘14, 523S/9

Industrieterrein ‘De Wetering’

Ambachtstraat 18

2861 EX Bergambacht/NL

Tel. (+31)(0)182 35 46 66

Fax (+31)(0)182 35 46 47

E-mail pols.aggregaten@wxs.nl

Internet www.pols-aggregaten.nl

# SOUNDPROOF VERSION

380/220 – 400/230 – 415/240 Volt – 3 Phase – 50 Hz – 1500 r.p.m.

| Model | Power Output P.R.P.(1) | Cyl. | Asp. | Engine model | Dimension mm | Weight Kg. | Fuel tank Cap. Lt. | LPS (**) dB(A) | DIGITAL Control Panel Manual/Auto Start MCB 4P | AMF system |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  | External ATS Panel Type CTI, max 160A Type ATI, max 630A |
|  | KVA | KW |  |  |  | Length | Width | Height |  |  |  | Price in EURO |
| P13.5-6 | 12,5 | 10 | 3 | NA | 403D-15G | 1.705 | 880 | 1.265 | 650 | 55 | 58,7 | Price on request | CTI/63A |
| P22-6 | 20 | 16 | 4 | NA | 404D-22G | 1.705 | 880 | 1.265 | 720 | 55 | 65,2 |  | CTI/63A |
| P33-3 | 30 | 24 | 3 | NA | 1103A-33G1 | 1.864 | 887 | 1.349 | 835 | 56 | 67 |  | CTI/63A |
| P50-3 | 45 | 36 | 3 | TC | 1103A-33TG1 | 2.291 | 1.026 | 1.426 | 1.025 | 145 | 62,1 |  | CTI/125A |
| P65-5 | 60 | 48 | 3 | TC | 1103A-33TG2 | 2.291 | 1.026 | 1.426 | 1.067 | 145 | 63 |  | CTI/125A |
| P88-3 | 80 | 64 | 4 | TC | 1104A-44TG2 | 2.291 | 1.126 | 1.426 | 1.202 | 188 | 65,2 |  | CTI/125A |
| P110-3 | 100 | 80 | 4 | TCA | 1104C-TAG2 | 2.761 | 1.126 | 1.535 | 1.400 | 212 | 71,3 |  | CTI/160A |
| P150-3 | 135 | 108 | 6 | TCA | 1006 TAG | 3.511 | 1.126 | 1.681 | 1.840 | 289 | 68 |  | ATI/250A |
| P165-3 | 150 | 120 | 6 | TCA | 1006 TAG2 | 3.511 | 1.126 | 1.681 | 1.840 | 289 | 69 |  | ATI/250A |
| P200-3 | 180 | 144 | 6 | TCA | 1106A-70TAG3 | 3.511 | 1.326 | 1.681 | 2.074 | 384 | 72 |  | ATI/400A |
| P220-3 | 200 | 160 | 6 | TCA | 1106A-70TAG4 | 3.511 | 1.326 | 1.681 | 2.159 | 384 | 72 |  | ATI/400A |

P13.5-6, P22-6 with Leroy Somer generator											** sound pressure level at 7 m./ 75% load/Prime

- P.R.P.:  Performance data refers to Standard Reference Conditions of ISO 8528: + 25°C, 100 m ALT, relative humidity 30%. During running-in period the output increases by approx. 5% which is taken into consideration at delivery. Power reduction acc. to DIN ISO 3046. Standard values: above 100 m ALT approx. 1% per 100 m. Above 25° C (77 ° F) approx. 4% per 10° C (50° F).

STANDARD		: P13.5-6, P22-6 	CAL    Soundproof

: P33-6 to P110-6 	CALG Soundproof

### : Electronic type governing : P110-3 to P220-3				Price: excl. VAT, ex works Bergambacht

### : Drip Tray		     : P33-3 to P220-3				Delivery time: on request

### : Digital Control Panel DCP-10						We reserve the right to change specifications without notice.

### OPTIONS ON REQUEST	: Bat. Charger, Pre heating resistance engine				Validity : 2014

### : Lube Oil Drain Pump, Radiator Low water level shutdown

### :  3 way Valve, Decanting Fuel Pump

: Remote, Monitoring and Control options

Op al onze offertes, op alle opdrachten aan ons en op alle met ons gesloten overeenkomsten zijn toepasselijk de METAALUNIEVOORWAARDEN, gedeponeerd ter Griffie van de Rechtbank te Rotterdam, zoals deze luiden volgens de laatstelijk aldaar neergelegde tekst. Zie bijlage

# Text boxes

F.G. WILSON

GENERATING SETS WITH

PERKINS ENGINE

MARELLI ALTERNATOR

*

*

*

Non-Emission Compliant EU

Excl. P13.5-6 and P22-6 – EU STAGE 3