BULLETIN              Mrt. ’16, 453/12

Industrieterrein ‘De Wetering’

Ambachtstraat 18

2861 EX Bergambacht/NL

Tel. (+31)(0)182 35 46 66

Fax (+31)(0)182 35 46 47

E-mail pols.aggregaten@wxs.nl

Internet www.pols-aggregaten.nl

| S CLASS PETROL: Versatility and reliability | NEW DESIGN ! |
| --- | --- |

| MODEL | S 5000 SHEPI | S 5000 THEPI | S 8000 SHEPI | S 8000 THEPI |
| --- | --- | --- | --- | --- |
| GENERATOR 3000 RPM |  | + AVR | + AVR |  | + AVR | + AVR |
| Three-phase power |
| Maximum Power LTP KW |  |  | 5.0 |  |  | 6.6 |
| Voltage Volt |  |  | 400 |  |  | 400 |
| Frequency Hz |  |  | 50 |  |  | 50 |
| Single-phase power |
| Maximum Power LTP KW | 4.8 | 3.7 | 6.4 | 4.9 |
| Voltage Volt | 230 |
| Frequency Hz | 50 |
| ENGINE |
| Model | HONDA |
| Type | GX270 | GX390 |
| Displacement cc | 270 | 389 |
| Cylinder | 1 | 1 |
| Power kW | 6.3 | 8.3 |
| Fuel | unleaded petrol |
| Aspiration | natural |
| Starting system | electric | electric | electric | electric |
| CONSUMPTION |
| Consumption g/kWh | 313 |
| Tank capacity l | 26,5 |
| Running time at 75% h | 16 | 12,3 |
| NOISE EMISSION |
| Noise LWA dB(A) | 97 | 97 | 97 | 97 |
| Noise pressure Level at 4 m. dB(A) | 73 | 73 | 73 | 73 |
| DIMENSIONS AND WEIGHT |
| L x W x H mm | 840 x 615 x 753 |
| Weight (dry) kg | 89 | 97 | 109 | 112 |
| Price EURO | On request |

- Transportation kit

- Battery Charger 12 Vdc/10A

Instrumentation:

- Voltmeter – Frequency meter – Hour counter – Fuel gauge

| S5000 Single Phase S8000 | - 1 x Socket CEE 230V 32A – 1 x Socket CEE 230V 16A – 1 x Schuko 230V 16A - Thermal Circuit Breaker – Differential Protection (DPP) – Oil Guard |  |
| --- | --- | --- |
| S5000 3-Phase S8000 | - 1 x Socket CEE 400V 16A (3P+N+T) – 1 x Socket CEE 230V 16A – 1 x Schuko 230V 16A - Thermal Circuit Breaker – Differential Protection (DPP) – Oil Guard |  |
| Accessories/options | - Remote control / RSS - AMF system |  |

Prices: excl. VAT

Delivery: ex Works Bergambacht

Op al onze offertes, op alle opdrachten aan ons en op alle met ons gesloten overeenkomsten zijn toepasselijk de METAALUNIEVOORWAARDEN, gedeponeerd ter Griffie van de Rechtbank te Rotterdam, zoals deze luiden volgens de laatstelijk aldaar neergelegde tekst. Zie bijlage.